## Slide 1: On Processor Design and Memory Models
Ofek Shilon
CppCon 2026

## Slide 2
Pseudo quote:
  “… the order in which mem operations become visible can be different than the program order…”?
Core Problem:
  Huh?

## Slide 3: Example Program
NEW --> data
R1 <-- ready
TRUE --> ready
R2 <-- data
if !R1: goto Load_R1
Writer Core
Reader Core

## Slide 4: Strict Consistency
NEW --> data
R1 <-- ready
TRUE --> ready
R2 <-- data
if !R1: goto Load_R1
Writer Core
Reader Core

## Slide 5: Sequential Consistency (SC)
NEW --> data
R1 <-- ready
TRUE --> ready
R2 <-- data
if !R1: goto Load_R1
Writer Core
Reader Core

## Slide 6: Sequential Consistency (SC)
NEW --> data
R1 <-- ready = TRUE
TRUE --> ready
R2 <-- data = NEW

## Slide 7: Sequential Consistency (SC)
NEW --> data
R1 <-- ready = FALSE
TRUE --> ready
R2 <-- data = NEW
R1 <-- ready = FALSE
R1 <-- ready = TRUE
R1 <-- ready = FALSE

## Slide 8: Why not SC?
What can cause cores to disagree on memory contents, at a specific point in time?
What can cause cores to disagree on order of memory operations?
What does it mean for a write to memory to be visible to all threads?

## Slide 9: Reasons

## Slide 10: Non-answer: private caches
Core
Core
Memory
L2/L3: Shared Caches
L1 Cache
L1 Cache

## Slide 11: Non-answer: private caches
Core
Memory
L1 Cache
deadcafe
deadcafe
deadc9fe
L1 Cache
deadcafe
Core

## Slide 12: Non-answer: private caches
Core
Memory
L1 Cache
deadcafe
deadc9fe
L1 Cache
deadcafe
Core
?
deadc9fe

## Slide 13: Cache Coherence
Cache line states:
Cache coherence protocols:
  MESI
  (MOESI, MESIF, ACE/CHI…)
Valid
Invalid
Modified
Exclusive
Shared
Invalid

## Slide 14: Answer #1: Invalidate queues
Core
Memory
L1 Cache
deadcafe
deadcafe
deadc9fe
L1 Cache
deadcafe
Core

## Slide 15: Answer #1: Invalidate queues
Invalidate
queue
Core
L1 Cache
L1 Cache
deadcafe
Core
deadcafe
deadc9fe
data? deadcafe
data? deadc9fe

## Slide 16: Answer #1: Invalidate queues
NEW --> data
R1 <-- ready
TRUE --> ready
R2 <-- data
if !R1 goto Load1
Writer Core
Reader Core
ready = TRUE
data = OLD

## Slide 17: Answer #2: non multi-copy atomicity
Core
L1 Cache
OLD
NEW
L1 Cache
OLD
Core
Core
L1 Cache
OLD
NEW
OLD

## Slide 18: Write Buffers
Core
L1 Cache
deadc9fe

## Slide 19: Write Buffers
L1 Cache
Core
NEW --> data
Write buffer

## Slide 20: Write Buffers
Caches + Memory
Core
NEW --> data
Core
data?
data?
NEW
OLD

## Slide 21: FIFO write buffers
Caches + Memory
Core
TRUE --> ready
NEW --> data
Core
data? OLD
ready? FALSE
data? NEW
ready? FALSE
data? NEW
ready? TRUE

## Slide 22: Dekker/Peterson Algorithm
TRUE --> taken1
TRUE --> taken2
R1 <-- taken2
R2 <-- taken1
taken1 = FALSE, taken2 = FALSE
Core
Core

## Slide 23: Dekker/Peterson Algorithm
TRUE --> taken1
TRUE --> taken2
R1 <-- taken2
R2 <-- taken1
TRUE
taken1 = FALSE, taken2 = FALSE
Core
Core

## Slide 24: Dekker/Peterson Algorithm
TRUE --> taken1
TRUE --> taken2
R1 <-- taken2
R2 <-- taken1
TRUE
taken1 = FALSE, taken2 = FALSE
Core
Core

## Slide 25: FIFO write buffers
taken1? FALSE
taken2? FALSE
Caches/Memory: taken1 = FALSE, taken2 = FALSE
Core
Core
TRUE --> taken1
TRUE --> taken2

## Slide 26: Intel Memory Model
TSO: Total Store Order :
  Stores cannot bypass other stores
  Loads can bypass older stores.
  [we didn’t discuss explicitly:] Stores cannot bypass older loads Loads cannot bypass other loads
Intuition: FIFO write buffers

## Slide 27: Coalescing write buffers
Coalesce writes to the same cache line

## Slide 28: Coalescing write buffers
Caches + Memory
Core
Core
dummy? 0 data? OLD ready? FALSE
TRUE --> ready
NEW --> data
1 --> dummy

## Slide 29: Coalescing write buffers
Caches + Memory
Core
Core
NEW --> data
1 --> dummy
TRUE --> ready
dummy? 0 data? OLD ready? FALSE
dummy? 1 data? OLD ready? TRUE

## Slide 30: Answers so far
Invalidate queues
Non multi-copy atomicity
Write buffers
  FIFO
  Coalescing

## Slide 31: Out of Order – Memory Ops
Instruction Queue
R1 = R1–R2
R4 --> [R2]
R2 = R3/R9
R3 <-- [R6]
R8 <-- [R1]
L/S
Addr
Val
Load-Store-Queue
Complete
Memory/Caches
0x10
L
S
R2
1234
L
R1
0x20
1234
Dispatch
Issue
/
R3
R9
RS1
RS2
RS3
Reservation Stations

## Slide 32: Out of Order – Memory Ops
Instruction Queue
R1 = R1–R2
R4 --> [R2]
R2 = R3/R9
R3 <-- [R6]
R8 <-- [R1]
L/S
Addr
Val
Load-Store-Queue
Complete
✓1
Memory/Caches
0x10
L
S
11
1234
0x20
L
R1
1234
Commit
R1:
R2:
R3:
R4:
Register File
5678
✓3
/
R3
R9
RS1
RS2
RS3
Reservation Stations
✓2
R3:5678
R2: 11
✓5
WB

## Slide 33: What could go wrong?
L/S
Addr
Val
Load-Store-Queue
Complete
L
0x10
L
0x30
Memory/Caches

## Slide 34: Answer #4: Out-of-Order Execution
NEW --> data
R1 <-- ready
TRUE --> ready
R2 <-- data
Writer Core
Reader Core
(=TRUE)
(=OLD!)
R2 <-- data

## Slide 35: More Rabbit Holes for the Curious
ROB (reorder buffer)
RAT (register alias table)
PRF (Physical Register File)
MOB (Memory Order Buffer)
Separation of LQ/SQ,
Virtual/physical addressing

## Slide 36: Answer #5: Speculative Execution
if (ready) {
R2 <-- data
…
Memory/Caches
TRUE
OLD

## Slide 37: Some Answers
What can cause cores to disagree on memory contents, at a specific point in time?
What can cause cores to disagree on order of memory operations?
   Invalidate queues, write buffers, out of order execution, speculative loads
What does it mean for a write to memory to be visible to all threads?
   To have the store commit, drained from the write buffer and finalize cache coherency propagation.

## Slide 38: Solutions
Fences, load-acquire, store-release, RMW

## Slide 39: Fences: Full
X86-64: MFENCE (Memory Fence)
ARM: DSB (Data Sync Barrier)
  Wait until previous stores are:
    Committed in the LSQ
    Drained from the write buffer
    Visible everywhere (invalidate requests processed)
  Wait until previous loads are retired
  Act as a speculation barrier
Safest + most expensive

## Slide 40: Fences: Full
ARM: DSB (Data Store Barrier)
ARM: DMB SY (Data Memory Barrier, System-wide)
Operation:
  Enforce ordering, not completion
  At: Write buffers, LSQ …
Cheaper alternative with mostly-compatible semantics
store
load
store
load

## Slide 41: ARM: Acquire / Release
dmb ld
dmb st
store
load
store
load
load
store

## Slide 42: ARM: Acquire / Release
dmb ld
dmb st
store
load
store
load
ldar – Load Acquire
stlr – Store Release
load
store

## Slide 43: ARM: Acquire / Release
NEW --> data
R1 <-- ready
R2 <-- data
if !R1 goto LoadReady
Reader Core
TRUE --> ready
Writer Core
stlr ready, TRUE
ldar R1, ready

## Slide 44: ARM: Acquire / Release
NEW --> data
R2 <-- data
if !R1 goto LoadReady
stlr ready, TRUE
ldar R1, ready
int data = 0;
std::atomic<bool> ready = 0;
void write() {
data = NEW;
ready.store(true,
memory_order_release);
}
int read() {
while (!ready.load(memory_order_acquire));
return data;
}

## Slide 45: C++ std::memory_order
For stores:
  memory_order_release
For loads:
  memory_order_acquire
  (==memory_order_consume)
For Read-Modify-Write (RMW) ops, such as +=:
  memory_order_acquire, memory_order_release
  memory_order_acq_rel: acquire AND release
For all:
  memory_order_relaxed: no order guarantees
  memory_order_seq_cst: full sequential consistency

## Slide 46: Read-Modify-Write
C++ atomic<> ops:
  +=, -=, &=, |=, ^=
    fetch_add(), fetch_sub(), fetch_and(), fetch_or(), fetch_xor()
  exchange()
  compare_exchange_weak(), compare_exchange_strong()
In assembly:
  X86-64: LOCK prefix (lock add, lock xchg)
  ARM: LL/SC
    + dedicated instructions, in ARM v8.1+

## Slide 47: Read-modify-write: x86-64
Core
L1 Cache
L1 Cache
deadcafe
deadcafe
deadc9fe

## Slide 48: Read-modify-write: x86-64
Core
L1 Cache
L1 Cache
deadcafe
L1 Cache
beadcafe
deadcafe
deadc9fe

## Slide 49: Read-modify-write: ARM
Core
L1 Cache
X
deadcafe
deadc9fe
LDXR
STXR

## Slide 50: Read-modify-write: ARM
Core
L1 Cache
X
deadcafe
LDXR
STXR
L1 Cache
beadcafe
Core
STR

## Slide 51: Read-modify-write: ARM
Core
L1 Cache
deadcafe
LDXR
STXR
  compare_exchange_weak(), compare_exchange_strong()

## Slide 52: Read-modify-write: ARM
LDXR/STXR extension:
  LDAXR – load-acquire exclusive register
  STLXR – store-release exclusive register
  Additionally enforce acquire/release ordering, same as LDAR/STLR
  Necessary to actually be usable in locks
Riddle: why is the exclusive monitor needed?
  Why not a special “store that fails if the dest cache line is invalidated”?

## Slide 53: Memory Models

## Slide 54: Recall:
Strong:
  Strict Consistency
  Sequential Consistency (SC)
Sort-of strong:
  TSO
    New loads can bypass old stores

## Slide 55: Relaxed Memory Model
RISC-V Weak Memory Ordering (RVWMO)
Processor Consistency (PC)
Release Consistency (RC)
…

## Slide 56: C++ Memory Model
Not this:

## Slide 57: C++ Memory Model
Sequential-Consistency for Data-Race-Free (SC-DRF)
  If the program has no data races, execution would appear to all threads as some interleaving of thread program-orders.
If a program is data-race-free, isn’t that obvious?

## Slide 58: C++ Memory Model
Two threads accessing the same memory, at least one of them writing to it
Two threads accessing the same memory, at least one of them writing to it, with no happens-before relation between the operations
Data conflict
Data race

## Slide 59: C++ Memory Model
Two threads accessing the same memory, at least one of them writing to it
Two threads accessing the same memory, at least one of them writing to it, with no happens-before relation between the operations
Data conflict
Data race
59

## Slide 60
https://www.cl.cam.ac.uk/~pes20/rems/

## Slide 61: REMS

## Slide 62: REMS
http://svr-pes20-cppmem.cl.cam.ac.uk/cppmem/

## Slide 63: REMS

## Slide 64: Out-of-Thin-Air (OOTA)
if (y == 1)
if (x == 1)
y = 1;
x = 1;
x = 0, y = 0
Allowed result: x = 1, y = 1
??

## Slide 65: Out-of-Thin-Air (OOTA)
if (x == 1)
y = 1;
if (y == 1)
x = 1;
x = 0, y = 0
else
x = 1;
x = 1;
Optimizing compiler
Allowed result: x = 1, y = 1
!!

## Slide 66: Summary
Different cores can have different views of memory because:
  Reasons
Software solves these problems by:
  Fences
  RMW
  OS level locks: futexes, mutexes etc.
Memory Models
  Your effort is probably better spent on understanding HW memory models

## Slide 67: Thanks for listening!
OfekShilon @

## Slide 69: Resources
High Performance Computer Architecture – Free online course by Milos Prvulovic of GeorgiaTech

## Slide 70: NT writes, Write-Combine Buffers
(Canonical) Example use case: zero a memory page
Telling the processor it is about to overwrite full cache lines
WCB: collect multiple writes before sending to the cache coherency system
Avoid the inefficient dance of RFO (Read-For-Ownership) request + modification + writeback.
MOVNT* instructions, do not undergo the usual coherency route – may be visible only some time in the future.

## Slide 71: Fences: Implicit
Instructions with some order-serialization side effects:
  x86/64:
    CPUID, IRET, RSM, LOCK *, …
  ARM:
    MSR, MRS, ERET, SVC, HVC, SMC …
Notes: instructions with order-serialization side effects, sometimes even stronger than fences

## Slide 72: Fences: Store
X86-64: SFENCE
  Controls completion
  Drain write buffer, stall until older stores are visible everywhere
  Reorder barrier
  Regular stores are already ordered! Mostly unneeded
  Impacts special non-cached store instructions (MOVNT*).
store
store

## Slide 73: Fences: Load
x86/64: LFENCE
  Block a younger read from issuing until all older reads have completed
    Completed = issued + resolved cache misses + retired
  Block speculative execution past the fence
    only in recent generations – 2018+ (since Spectre)
load
load

## Slide 74: “Pipeline”?
Fetch
Decode
Issue
Exec
Write
Commit
…
Fetch
Decode
Issue
Exec
Write
Commit
Fetch
Decode
Issue
Exec
Write
Commit
Fetch
Decode
Issue
Exec
Write
Fetch
Decode
Issue
Exec
Fetch
Decode
Issue
Fetch
Decode
Fetch

## Slide 75: “Pipeline”?
…
Fetch
Decode
Issue
Fetch
Decode
Issue
Fetch
Decode
Issue
Fetch
Decode
Issue
Fetch
Decode
Issue
Fetch
Decode
Issue
Fetch
Decode
Fetch
Commit
Commit
Commit
Commit
Commit

## Slide 76: Out of Order Execution
R1 = R2 + R3
R4 = R1 – R2
R1 = R2 / R3
R2 = R4 + R1
Fetch
R1: 2
R2: -1
R3: 3
R4: 1
Register File
ADD
Issue
MUL
RS1
RS2
RS3
RS4
RS5
Instruction Queue

## Slide 77: Out of Order Execution
R1 = R2 + R3
R4 = R1 – R2
R1 = R2 / R3
R2 = R4 + R1
R1: 2
R2: -1
R3: 3
R4: 1
Register File
ADD
Register Alias Table (RAT)
R1:
R2:
R3:
R4:
Issue
MUL
RS1
RS2
RS3
RS4
RS5
+
1
2
V
R2: RS1
Fetch
Instruction Queue

## Slide 78: Out of Order Execution
R1 = R2 + R3
R4 = R1 – R2
R1 = R2 / R3
R1: 2
R2: -1
R3: 3
R4: 1
Register File
ADD
Register Alias Table (RAT)
R1:
R2:
R3:
R4:
MUL
RS1
RS2
RS3
/
RS4
RS5
+
1
2
V
R2: RS1
Issue
R2
R3
3
RS1
Dispatch
R1: RS4
Instruction Queue

## Slide 79: Out of Order Execution
R1 = R2 + R3
R4 = R1 – R2
R1 = R2 / R3
R1: 2
R2: -1
R3: 3
R4: 1
Register File
ADD
Register Alias Table (RAT)
R1:
R2:
R3:
R4:
MUL
RS1
RS2
RS3
/
RS4
RS5
+
1
2
V
R2: RS1
R2
R3
3
RS1
Broadcast
R2: 3
Commit
3
V
R2:
Instruction Queue

## Slide 80: Out of Order Execution
R1 = R2 + R3
R4 = R1 – R2
R1 = R2 / R3
R1: 2
R2: -1
R3: 3
R4: 1
Register File
ADD
Register Alias Table (RAT)
R1:
R2:
R3:
R4:
MUL
RS1
RS2
RS3
/
RS4
RS5
+
1
2
V
R2: RS1
R2
R3
3
RS1
Broadcast
R2: 3
Commit
3
V
R2:
Fetch
Branch Prediction

## Slide 81: Out of Order Execution
Instruction Queue
R1 = R2 + R3
R4 = R1 – R2
R1 = R2 / R3
R2 = R4 + R1
Fetch
R1: 2
R2: -1
R3: 3
R4: 1
Register File
ADD
+
1
2
V
RS1
RS2
RS3
Issue
Dispatch
Register Alias Table (RAT)
R1:
R2: RS1
R3:
R4:
R2: ROB3
R2:
*
*
*
*
reg
val
done
Reorder Buffer (ROB)
ROB1
ROB2
ROB3
ROB4
ROB5
V
V
R2: 3
R2
3
V

## Slide 82: Terminology
Issue
Dispatch
Commit
Allocate, Dispatch
Execute, Issue
Complete, Retire, Graduate